## Slide 1: Implementation of an Open-source Tool for Aeroelastic Simulations of Horizontal Axis Wind Turbines
Master thesis presentation

## Slide 2: Index:
Objectives
Structural module
Aerodynamic module
Implementation
Validation
Questions

## Slide 3: Objectives:
Implement a simple open-source aeroelastic tool, (HarPy), for the simulation of horizontal axis wind turbines under steady and turbulent wind inflow conditions in the time domain.
Complete enough to achieve reasonably accurate results.
Simple enough to allow a straightforward connection between the basic concepts, problem physics, model assumptions, key equations, the algorithm and the implemented code.
The code must be open-source and free so the use of the code would not be a barrier to the use, customisation and expandability of the code.

## Slide 4: Wind turbine reference kinematics:
The complete turbine dynamics is obtained using 1 inertial and 4 moving reference of frames.
Structural module

## Slide 5: Wind turbine reference kinematics:
The complete turbine dynamics is obtained using 1 inertial and 4 moving reference of frames.
Structural module
Reference frames
I0 : Inertial
I1 : Tower-top
I2 : Shaft bearing
I3 : Shaft tip
I4 : Blade root
Transformation matrices:

## Slide 6: Blade kinematics:
The turbine blades displacement is described using a linear combination of its mode shapes.
Structural module
edgewise
flapwise
Stiff radially

## Slide 7: Nacelle and shaft kinematics:
The tower top and shaft tip displacements are modelled using linear and angular stiffness.
Structural module

## Slide 8: Wind turbine reference kinematics:
The position and absolute velocity of the blades sections are then obtained.
Structural module

## Slide 9: Energy equations:
To derive the equations of motion using the Lagrange method is necessary to derive the kinetic and potential energy of the wind turbine and the work done by non-conservative forces.
Structural module

## Slide 10: Lagrangian mechanics:
In Lagrangian mechanics, the equations of motion of a system are derived by solving the Lagrange equations.
The Lagrange method often offer a more straightforward and convenient method to implement on symbolic computational tools.
Structural module

## Slide 11: Symbolic implementation:
The symbolic derivation was carried out in Python using the symbolic manipulation package Sympy.
A code generator was adapted to translate the symbolic equations into numerical code and generate the structural module code automatically.
numpy.trapz(self.m*self.phi_x[0,:]**2,self.z)
Structural module

## Slide 12: Symbolic derivation:
Structural module

## Slide 13: Numerical code output:
Structural module

## Slide 14: Aerodynamic module:
The wind turbine aerodynamics is modelled using the unsteady Blade Element Momentum theory under yaw.

## Slide 15: Dynamic inflow:
The wind velocity induced by the rotor on flow is calculated using the two filters dynamic inflow model proposed by Stig Øye .
Aerodynamic module

## Slide 16: Yaw / Tilt correction:
The wake skew angle effect on the induced wind velocity is calculated using the model proposed by Glauert as referenced in [18] and [35].
Aerodynamic module

## Slide 17: Dynamic stall model:
The dynamic stall is modelled using the separation factor fs between the inviscid and the fully separated lift coefficients proposed by Stig Øye.
Aerodynamic module

## Slide 18: Numeric tool:
Implementation
Wind Box
Wind Turbine
Wind turbine structural
Simulation object
Controllers
Model Script
Create objects
Create differential equation
Time integration
The software code is implemented in Python using the object-oriented concept, organising the attributes and functions into classes of objects.

## Slide 19: Study cases:
In order to evaluate the implementation, the results given by the project aeroelastic code under different load scenarios were compared with DTU’s aeroelastic code HAWC2.
Validation

## Slide 20: Case 1.0:
Validation

## Slide 21: Case 1.1:
Validation

## Slide 22: Case 1.2:
Validation

## Slide 23: Case 1.3:
Validation

## Slide 24: Case 1.4:
Validation

## Slide 25: Case 2.0:
Validation

## Slide 26: Case 2.1:
Validation

## Slide 27: Questions
Discussion